| Air Compressor | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 041SOP | 038RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Unrestrained air hose whipping around; Material blown under pressure; Noise; slips, trips & falls; Hazardous Manual Tasks |
|  |  |  | Rings & Jewellry must not be worn |  |
| PRE-OPERATIONAL SAFETY Ensure the work area is well ventilated and not interfering with other students or activities. Visually check all air hoses and electrical leads used with the compressor for damage and slip/trip hazards. Ensure all guards for the compressor (e.g. belt and pulley cover) are in place and in good working order. Ensure you are familiar with the operation of the ON/OFF switch. Check that the regulator is set to the appropriate pressure for the activity. Check the oil level of the compressor in the oil sight glass |
| OPERATIONAL SAFETY PRECAUTIONS Ensure all attachments used with the air compressor are in good condition before using. Be careful when attaching and disconnecting tools to the air hose. Hold the air hose and tool firmly during this process. Check the compressor regularly, noting pressure increase and cut-out/cut-in pressure. Listen for any air leaks from any flexible airlines and immediately report any leaks. Adjust pressure regulator to suit work requirements Turn off and disconnect air hoses and electrical leads after use. Never leave air compressor and equipment unattended. |
| HOUSEKEEPING Leave the work area in a safe, clean and tidy state – remove any waste. Release condensation from the drain before storing away Air hoses and electrical leads should be coiled with large loops. FORBIDDEN Never use compressed air to clean off clothes, workbenches or floor surfaces Never direct compressed air at your body or another person. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.