| Arc Welding | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 046SOP | 041RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Welding flash - eye injury; Burns; Electric Shock. |
| PRE-OPERATIONAL SAFETY Ensure the welder is used in a suitable safe work area. Ensure all cables are correctly fastened, free of cracks and splits and unwound before work. Keep the area clean & free of grease, oils & flammables. Ensure other workers are protected from any UV flash. Ensure the area is well ventilated (with fume extraction as required). |
| OPERATIONAL SAFETY CHECKS Ensure the welder is correctly set up for current, voltage and good earth. Ensure that other workers in this locality are protected from any UV & IR radiation flash. Always close the UV curtain to the welding bay or erect a UV screen. Ensure the welding return cable (earth) makes firm contact to provide a good electrical contact. Ensure your work-piece has been prepared to be free of any paint, oxides or other surface finishes ensuring a good electrical contact. Take particular care to avoid accidental UV welding flash to the skin or eyes. Never leave the welder running unattended. Regularly inspect the welding tip and shield for damage. When welding is finished or interrupted, turn off the welder and secure the handpiece safely. Ensure the work area can isolate hot areas from workers to avoid hot surfaces until job is cool. |
| HOUSEKEEPING Ensure the welder is switched off (and fume extraction if used). Check for any damage to welder and cables at the end of job. Wind up cables. Hang up the welding handpiece and cables securely. Check contact points for damage or corrosion. Leave the work area and welding bench in a safe, clean, and tidy condition. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.