| Bandsaw | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 042SOP | 039RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Foreign body in eyes; severe lacerations / cuts; Electric shock; crush injuries. |
|  |  |  |  | Rings & jewelly must not be worn |  |
| PRE-OPERATIONAL SAFETY Ensure no slip/trip hazards are present in workspaces and walkways. Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop. Check that all guards are in position. Ensure push stick is available. Lower the blade guide and guard to full effect. Start the dust extraction unit before using the saw. Faulty equipment must not be used. Immediately report suspect machinery. |
| OPERATIONAL SAFETY CHECKS Never leave the machine running unattended. The work piece should be fed forward evenly and held firmly on the table to ensure effective control during cutting whilst keeping hands in a safe position. Use a push stick when feeding material past the blade. Do not force a wide blade on a cut of small radius. Use relief cuts when cutting sharp curves. Before making adjustments switch off the saw and bring the machine to a complete standstill. Stop the machine before attempting to back the work away from the blade. Stop the saw immediately if the blade develops a ‘click’. Report it to your Supervisor / Manager. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.