| Belt and Disc Sander | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 052SOP | 048RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Abrasions; Burns to Skin; Eye Injuries; Excessive Dust; Flying Objects, Electric Shock; |
|  |  |  | Rings and jewellery must not be worn. | Gloves must not be worn when using this machine. |  |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure no slip/trip hazards are present. Ensure you are familiar with the operation of the ON/OFF starter and E-Stop (if fitted). Check the table is set not more than 2mm from disc. Check belts and discs are in a serviceable condition. Operator must be positioned out of direct line of abrasive belt at all times. Ensure dust extraction is on before operating machine. Faulty equipment must not be used. Immediately report suspect machinery. |
| OPERATIONAL SAFETY PRECAUTIONS Allow machine to reach maximum revolutions before operating to avoid overloading. Always place material on the table on the downward side of the disc travel to hold it down on the table surface. Hold material firmly against stops or table before applying pressure on abrasive. Keep fingers clear of disc or belt while sanding. Never leave the machine while it is running. Before making adjustments switch off and bring the machine to a complete standstill. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.