| Belt Sander - Fixed | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 045SOP | 041RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Abrasions; Foreign body in eyes;; Electric shock; excessive dust. |
|  |  |  |  | Gloves, Rings & jewelly must not be worn |  |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure no slip/trip-hazards are present. Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop (if fitted). Check the table is set not more than 2mm from disc. Check abrasive disc is in a serviceable condition. Start the dust extraction unit before using the machine. Faulty equipment must not be used. Immediately report suspect equipment. |
| OPERATIONAL SAFETY CHECKS Allow machine to reach maximum revolutions before operating to avoid overloading. NEVER attempt to sand very small items, lift or tilt the material while sanding. Always place material on the table on the downward side of the disc travel and hold it securely on the table surface. Hold material firmly against the table before applying pressure on abrasive disc. Keep hands/fingers clear of abrasive disc while sanding. NEVER attempt to or try to sharpen metal items. NEVER leave the machine running unattended. Before making adjustments switch off and bring the machine to a complete standstill. FORBIDDEN Attempting to sand very small items Attempting to sharpen tools Attempting to sand metal |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.