| Chainsaw - Petrol | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 067SOP | 069RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Cuts and lacerations / Hearing loss / Flying debris / Eye injuries / Entanglement / Crush injuries / Death |
| PRE-OPERATIONAL SAFETY Ensure the chainsaw is clean. Check for loose, worn or damaged parts. (Do not operate till repaired / replaced) Inspect fuel lines, carburettor for leaks. (Do not operate till repaired / replaced) Check effectiveness of chain brake and operating controls. Ensure safety guards and other safety features are secure and functioning) Ensure chain is sharp and correctly tensioned. Ensure you are in good physical condition to operate chainsaw. Ensure PPE is available and fits correctly. |
| OPERATIONAL SAFETY PRECAUTIONS Follow all safety precautions in the operator’s manual – improper use can cause serious or fatal injuries. Ensure area is clear of obstructions / other personnel. Start chainsaw resting on the ground. Maintain balance and secure footing when operating. Start cut with chainsaw at full speed and bumper is in contact with work piece. Be aware of the guide bar nose at all times when chain is in motion. Pay full attention at all times and be alert for movement of the work piece. Apply chain brake when chainsaw is at rest. Never use chainsaw over or above shoulder height. Allow chainsaw to cool before refuelling. |
| HOUSEKEEPING Clean chainsaw at completion of task. Sharpen saw chain as per manufacturer’s requirements. Service chainsaw as per manufacturer’s recommendations. Keep work area clean and tidy. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.