| Cold Cut Saw | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 048SOP | 044RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Shattering Blade; Airborne dust; Eye injuries; Contact with blade at point of operation; Material slipping in vice/clamp |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure that no slip/trip-hazards are present. Check that all safety guards are in position and are set to the minimum clearance from the workpiece being cut. Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop (if fitted). Ensure all locks are securely tightened. Ensure table and work area is clear of all tools, off-cut metal. Faulty equipment must not be used. Immediately report suspect equipment. |
| OPERATIONAL SAFETY PRECAUTIONS Do not cut freehand, clamp material firmly in vice. Allow the saw blade to obtain maximum speed before making a cut. Make sure cooling fluid is flowing over saw blade. Always stand to one side of the line of cut. Never remove off cuts from the saw table while the saw is running. Before making adjustments switch off and bring the machine to a complete standstill. Never leave offcuts on saw table while cutting. Do not clamp material shorter that the width of clamping vice. Ensure long material is supported on the right side of machine. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.