| Compound Mitre Saw | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 049SOP | 045RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Rotating & Moving Parts; Pinch & Squash Injuries; Flying Chips and Debris; Eye Injuries |
| PRE-OPERATIONAL SAFETY Ensure the saw is properly secured to a workbench by bolts/ clamps at approximately hip height. Ensure the saw is operated on an RCD protected circuit. Check workspaces and walkways to ensure no slip/trip-hazards are present. Check that all safety guards are in position and are operational. Ensure you are familiar with the operation of the ON/OFF DOL switch and Emergency stop. Keep table and work area clear of all tools, off-cut timber and sawdust. Start the dust extraction unit before using the machine. Faulty equipment must not be used. Immediately report suspect equipment. Complete On Guard Safety training and submit to teacher. |
| OPERATIONAL SAFETY PRECAUTIONS The maximum cut for the machine must not be exceeded. Ensure all adjustments are secure before making a cut. Use clamps to secure and support the workpiece to a stable platform. Do not use a length stop on the free scrap end of a clamped workpiece. Do not cut more than one workpiece at a time. Before turning on the saw, perform a dry run of the cutting operation to ensure that no problems will occur when the cut is made. Do not start the saw with the blade touching the workpiece. Allow the blade to reach full speed before contacting the workpiece. Avoid reaching over the saw line. Do not cross arms when cutting. Always use the right hand to pull the saw down, keep the left hand, especially the thumb well clear of the line of cut. If workpiece is bowed or warped, clamp it with the outside bowed face toward the fence. After finishing the cut, release the switch, hold the saw arm down and wait for blade to stop before removing work or off-cut piece. Disconnect the plug from the power source and bring the machine to a complete standstill before making any adjustments. |
| HOUSEKEEPING Switch off and lock out the machine. Leave the machine in a safe, clean and tidy stat |
| Date of last review: | Signature: |