| Cut Off Saw | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 051SOP | 044RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Moving, rotating and sharp parts; Dust and fumes; Electricity Pinch and crush; Eye injuries; Noise; Burns and hot ejected waste material |
| PRE-OPERATIONAL SAFETY Ensure the power tool has a suitable safe work area. If changing cut-off wheel, check for appropriateness and arbor hole size. Inspect the cut-off wheel for chips and cracks. Check that the guards are all in place and in good working order. If fitted with a depth stop, ensure that it is in proper adjustment/alignment. Familiarise yourself with the operation of the ON/OFF switch. Ensure your work area is clear of slip/trip hazards and flammable materials. |
| OPERATIONAL SAFETY PRECAUTIONS Ensure all adjustments to the machine are secure before making a cut. Do not hold your work piece by hand. It may become very hot while being cut. Use the vice to clamp the work and properly support any overhanging portion so the work piece is level with the base of the machine. Do not use a length stop on the free off-cut end of a clamped work piece. Allow the machine to reach full speed before contacting the work piece. Do not have any part of your body in line with the path of the abrasive disc. Ease the abrasive disc against the work piece when starting. Do not force tool. Keep hands away from cutting. Do not attempt to remove cut material while the abrasive wheel is moving. After finishing the cut, release the switch, hold the saw arm down and wait for the disc to stop before removing your work piece or off-cut piece. Before making any machinery adjustments, bring the machine to a complete standstill, and then disconnect the AC plug from the power source. |
| HOUSEKEEPING Ensure ventilation openings and switches are kept clean and free of foreign matter. Leave the work area in a safe, clean and tidy condition. |
| Date of last review: | Signature: |