| Drill Press | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 053SOP | 050RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Entanglement in rotating spindle or drill; Eye injuries Flying swarf or chips; Sharp edges & burrs; Hot surfaces or drill bits |
| PRE-OPERATIONAL SAFETY Check workspace and walkways to ensure no slip-hazards are present. Check that the drill chuck guard is in position. Ensure the chuck key (if used) has been removed from the drill chuck. Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop. Follow correct clamping procedures to ensure work is secure. If the job obstructs the walkway erect a barricade. Adjust spindle speed to suit drill, cutter diameter and type of material. Faulty equipment must not be used. Immediately report suspect equipment. |
| OPERATIONAL SAFETY PRECAUTIONS Never leave the Drill Press while it is running. Before making adjustments or before cleaning accumulated swarf, switch off and bring the machine to a complete standstill. Feed downwards at a sufficient rate to keep the drill cutting. Feed with care as the drill breaks through the underside of the work. Use a safe working posture. Beware of clothing or hair catching in the drill chuck or bit. |
| HOUSEKEEPING Never leave the Drill Press while it is running. Before making adjustments or before cleaning accumulated swarf, switch off and bring the machine to a complete standstill. Feed downwards at a sufficient rate to keep the drill cutting. Feed with care as the drill breaks through the underside of the work. Use a safe working posture. Beware of clothing or hair catching in the drill chuck or bit. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.