| Electric Sander - Handheld | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 071SOP | 074RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Cuts and abrasions / Exposure to Dust / Exposure to projectiles / Moving parts and electrical hazard |
| PRE-OPERATIONAL SAFETY Task (e.g. Drawings, instructions, specifications etc.) is clearly understood. 2. Ensure work piece is securely clamped. 3. Identify location of ON / OFF switch. 4. Faulty equipment must not be used. 5. Ensure dust extractor bag is empty and attached. 6. Ensure Power supply is off when connecting or disconnecting. |
| OPERATIONAL SAFETY PRECAUTIONS Do not leave running machinery unattended. Hold orbital sander securely. Secure work where possible. Use light pressure to allow machine to cut freely. Allow orbital sander to stop before lifting from work. |
| HOUSEKEEPING Return sander to storage area. Ensure good housekeeping practices are in place to minimise waste build-up. Sweep down bench and tidy work area. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.