| FORKLIFTS | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 084SOP | 090RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Tip overs, Collisions, Overloading, Pedestrians, Unstable ground, Overhead Obstructions, Combustibility due to gases, Poorly maintained forklift / attachments. |
| PRE-OPERATIONAL SAFETY Locate and ensure you are familiar with all machine operations and controls. Check brakes, lights and horn before use. Ensure reversing beeper and warning lights are operational. Ensure seat belt/safety restraint is in good condition. Know the capacity of the forklift before using it. Do not use a forklift without a load rating plate. Check gas-powered vehicles for gas leaks in fuel lines. Ensure the lifting forks are in sound condition and centred either side of the mast. Check tyre pressures. Never drive with a flat or under-inflated tyre. |
| OPERATIONAL SAFETY PRECAUTIONS Watch out for pedestrians. Ensure the lifting tines are secure into the pallet and the load is stable before lifting or driving off. Be careful of ceiling clearance or overhead obstructions when raising the mast. Always remember that the safe working load of a forklift reduces as the mast is tilted forward. Always put the heavy end of the load against the load backrest. When approaching a blind corner, use horn and drive slowly. Always have someone guide you if a load restricts your vision. Slow down when changing direction or on wet or greasy surfaces. Avoid harsh braking, especially when carrying a load. |
| HOUSEKEEPING When stopping the forklift: Park on even ground and lower the forks to the ground. Shift the gear selector to park position and apply the parking brake. Turn off the ignition and remove the keys. For gas-powered vehicles, turn off gas and don’t park near an ignition source, doorway or pit. REFUELLING For gas-powered vehicles, change gas bottles in a well-ventilated area clear of a naked flame or source of ignition. For battery-operated vehicles, charge in well-ventilated area. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.