| Grinder (Bench) | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 043SOP | 088RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Rotating and sharp parts; Electricity; Noise; Pinch and squash Dust and fumes; Eye injuries; Burns and hot ejected waste material |
|  |  |  |  | Rings & jewelly must not be worn |  |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure no slip/trip hazards are present. Ensure all guards and safety shields are in position before starting the grinder. Ensure that the wheels do not touch the work rest and that the gap between wheel and rest is no greater than 1.5mm. Check that wheels are running true and are not glazed or loaded. Locate and ensure you are familiar with the operation of the ON/OFF starter. Faulty equipment must not be used. Immediately report any suspect machinery. |
| OPERATIONAL SAFETY CHECKS Stand to the side of the wheels when starting up. Let the wheels gain maximum speed before starting to grind. Do not grind on the side of the wheel. Small objects must not be held by hand. Never leave the machine running unattended. Do not bend down near the machine whilst it is running. Never force the work-piece against a wheel. Slowly move the work-piece across the face of the wheel in a uniform manner. Coolant spilt on the floor should be immediately absorbed. |
| HOUSEKEEPING Switch off the grinder. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.