| High Pressure Cleaner | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 032SOP | 096RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Sprains / Strains; Electric Shock; Slip / Trip / Fall; Burn; Bruising |
| PRE-OPERATIONAL SAFETY Check all parts and cords for any damage before use. Unwind high pressure hose fully from the hose drum. Use only attachments supplied and approved by the manufacturer. Wear appropriate PPE. |
| OPERATIONAL SAFETY PRECAUTIONS The high pressure cleaner must not be directed at other people, animals or live electrical equipment. Sweep or brush all loose dirt and debris from the surface you are about to clean. Once all equipment is in position, connect to a water supply and ensure safety signs are on display Check the hoses are free of clogs and kinks and start up pressure washer. Start from a designated work area (building side) working outward when cleaning outside. Hold pressure washer wand with both hands and work the wand from shoulder to shoulder, slowly moving forwards. Do not swing the wand side to side in fast and erratic movements. Ensure firm footing and hold the spray handgun and spray lance firmly in both hands whilst in operation. |
| HOUSEKEEPING Turn off appliance and press the lever to release any remaining pressure in the system. Disconnect the appliance from water supply Store the handgun and spray lance in the accessory point and store appropriately |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.