| Mig Welding | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 047SOP | 043RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Welding flash - eye injury; Burns; Electric Shock; fire; fumes |
| PRE-OPERATIONAL SAFETY Check workspace, walkways and work leads to ensure that no slip/trip hazards are present. Check work area is clean and free of grease, oil and flammable material. Ensure the equipment and work area is dry to avoid electric shocks. Check gloves, welding gun and work leads are in good condition. Ensure the fume extractor unit is on before welding commences. Close the UV curtain or erect safety screens to ensure the protection of others. |
| OPERATIONAL SAFETY CHECKS Ensure machine is correctly set up for current, voltage, wire feed and gas flow. Ensure work return cables make firm contact to provide a good electrical connection. Ensure the work piece has been prepared to be free of any paint, oxides, or other surface finishes ensuring a good electrical contact. Close curtains and ensure all bystanders are wearing proper PPE Never leave the welder running unattended. Avoid welding flashes. Erect UV safety curtains as required. Regularly inspect the welding tip and shield for damage. When welding is finished or interrupted, turn off the shielding gas at the regulator, turn off the machine and secure the handpiece. |
| HOUSEKEEPING Switch off the machine and fume extraction. Close gas cylinder valve. Hang up the welding gun and welding cables. Leave the work area in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.