| Pallet Jack - Handheld | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 089SOP | 102RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Hydraulic fluid under pressure, Hazardous Manual Tasks – equipment & material, Slips, trips and falls, Heavy loads. |
| PRE-OPERATIONAL SAFETY Ensure your work area is well ventilated and not interfering with other students/activities. Visually check the condition of the trolley jack for damage. Check that the jack is labelled with a sticker indicating that it meets Australian standards – AS/NZS 2615. Familiarise yourself with the safe operation of this pneumatic trolley jack i.e. ensure you can safely raise and lower the jack. Ensure the floor surface you are rolling the jack on is hard, level and unobstructed. Familiarise yourself with the safe working limit of the trolley jack. |
| OPERATIONAL SAFETY PRECAUTIONS Ensure raised vehicles are supported with vehicle support stands. No person should get bodily under a vehicle supported by a hydraulic trolley jack. Read the vehicle manufacturer’s owner’s manual before lifting the vehicle. The wheels of the vehicle remaining on the ground should be chocked before the lifting operation proceeds. No person should be in the vehicle during the lifting process. The load should be centrally located on the head cap for the lift process. The trolley jack should be used to raise and lower only. Ensure that lubrication or other maintenance of the trolley jack is carried out according to the manufacturer’s instructions. |
| HOUSEKEEPING Leave the work area in a safe, clean and tidy condition. Ensure trolley wheels and jack handle are well maintained. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.