| Pan Brake | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 064SOP | 065RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Sharp Edges and Burrs / Impact from Counterweight / Squash/crush and pinch points |
| PRE-OPERATIONAL SAFETY Guards or safety devices shall never be removed or adjusted, except by an authorized person for maintenance purposes. Working parts should be well lubricated and the jaws and fingers free from rust and dirt. Ensure no slip/trip hazards are present in workspaces and walkways. Be aware of other personnel in the immediate vicinity and ensure the area is clear before using equipment. Familiarise yourself with and check all machine operations and controls. Faulty equipment must not be used. |
| OPERATIONAL SAFETY PRECAUTIONS Only one operator using the machine – school staff member to assist if required Never use pan brakes for bending metal that is beyond the machine’s capacity with respect to thickness, shape, or type. Never attempt to bend rod, wire, strap, or spring steel sheets in a pan brake. Remove the pan brake fingers that are in the way - use only the pan brake fingers required to make the bend. Ensure the pan brake fingers that are not removed for an operation are securely seated and firmly tightened before the machine is used. Ensure fingers and limbs are clear before operating the pan brake. Lower finger clamps to work - do not drop. Check work piece is secure & keep clear of moving counterweight (where fitted). |
| HOUSEKEEPING Lower finger clamps to a safe position - down position resting on base plate. Return all accessories to storage racks. Lock-out the action of the pan brake when not in use eg a system to lock handle & bending beam from use. Leave the work area in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.