| Panel Saw | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 065SOP | 066RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Cutting hands / Pinch & squash injuries / Flying chips and debris / Eye injuries / Excessive noise |
| PRE-OPERATIONAL SAFETY Clear the area around the machine. Locate and check the operation of the emergency stop. Check the blade condition and type is correct for the task. Check riving knife is correctly set and securely mounted. Do not store tools and parts on top of the machine. The fence must be set for all use of the machine. The guard should be set as low as possible. Where auto adjusting, the saw blade guard should return to the table without assistance. Faulty equipment must not be used. |
| OPERATIONAL SAFETY PRECAUTIONS Stand to one side when turning on power and feeding material past blade. Never leave the machine while it is still running. Check material being machined for nails and loose knots etc. Do not force materials past saw blade. Wait for the machine to stop and isolate before making any adjustments. Do not place your hands in line with the cut. Use a push stick for material less that 150mm wide and to remove offcuts. Do not attempt to remove off-cuts or saw dust from the table with your hands when the blade is in motion. |
| HOUSEKEEPING Switch off and lock out the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.