| Plasma Cutter | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 068SOP | 071RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Electric shock / Radiation burns / Body burns / Noxious gas / Compressed air / Fumes / Flying sparks and falling dross / Noise |
| PRE-OPERATIONAL SAFETY Check workspace and walkways to ensure that no slip / trip hazards are present. Check work area is clean and free of grease, oil and flammable material. Ensure the equipment and work area is dry to avoid electric shocks. Check gloves, welding gun and work leads are in good condition. Examine the material to see if it is to be cut free from hazards. Ensure the fume extractor unit is on before welding commences. Close the welding bay curtains to ensure the protection of others from flashes. |
| OPERATIONAL SAFETY PRECAUTIONS Ensure machine is correctly set up for current, voltage, wire feed and gas flow. Ensure work return cables make firm contact to provide a good electrical connection. Metals coated with or containing materials that emit toxic fumes should not be heated or cut unless coating is removed from the work surface. Do not weld or cut containers that have held combustible liquids or gases. Never leave the plasma cutter running unattended. |
| HOUSEKEEPING Switch off the machine and fume extraction (where used). Turn off air supply and hang up handpiece, hose and welding cables. Leave the work area in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.