| Polishing Machine (Buff) | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 069SOP | 072RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Work can be snatched if improperly presented to buff. Hair / clothing entanglement in moving machine parts / Eye injuries |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure no slip / trip hazards are present. Locate and ensure you are familiar with the operation of the ON / OFF starter. Both ends of the machine spindle must be covered at all times. Use appropriate mop type and polishing compound for the task. Faulty equipment must not be used. |
| OPERATIONAL SAFETY PRECAUTIONS Never leave the machine running unattended. Do not bend down near machine whilst it is running. Use the front of the wheel only. Work only below the centre of the spindle. Small work must be securely supported with a wooden backing. Work should be held so that edges cannot catch. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.