| Scaffolding - Portable | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 072SOP | 075RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Collapse of scaffold / Incorrect assembly / Manual handling / Struck by falling objects / Slips/trips/falls / Noise / Exposure to weather / Sprains/strains / Electrocution |
| PRE-OPERATIONAL SAFETY Ensure all components are well-maintained. Do not use components that are in poor condition. Do not mix components from differently branded scaffolding systems. Read and follow the manufacturer’s specifications, assembly instructions and warning labels. Inspect scaffold before its first use and at the start of each day. Ensure scaffold remains level and plumb at all times Use barricades, danger tags or warning signs to prevent unauthorised access. Ensure edge protection (hand rails, mid-rails and toe boards) is provided. Wear appropriate personal protective equipment. Do not work during a storm, wet conditions or high winds. |
| OPERATIONAL SAFETY PRECAUTIONS Castor brakes are to be applied at all times while the mobile scaffold is stationary. Access is to be only by way of an internal ladder. No climbing is allowed on the scaffold itself. Only work on fully planked work platforms. Ensure that working platforms are kept clear of debris and obstructions along their length. Do not leave tools and equipment on scaffolds. Scaffold is not to be moved while workers are on the scaffold work platform. Limit the number of workers on a scaffold at any one time. Do not exceed the safe working load of the scaffold. Do not make any unauthorised alterations to the scaffold. Do not permit workers or other persons to stand directly below a scaffold. Do not drop materials from the platforms. Do not fix high voltage leads and cables to the scaffolding. Never use ladders or makeshift devices on top of scaffolds to increase height. |
| HOUSEKEEPING Check and maintain all scaffold parts. Repair or discard and replace any damaged pieces immediately. Lubricate moving parts of all fittings. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.