| Table Router | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 075SOP | 078RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Material kickback / Flying chips and debris / Eye injuries / Excessive noise / Contact with cutter at point of operation and during cleaning and adjustment |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure no slip / trip hazards are present. Locate and ensure you are familiar with the operation of the ON / OFF starter and E-Stop (if fitted). Use only materials free from defects. Ensure cutter size conforms to machine specification. Machine must be isolated while cutters are being installed. Ensure all cutters are sharp and free of resin build up. Check cutter for clearance of rotation before starting machine. Adjust fence, guards and extraction for maximum protection and efficiency. Do not store tools and parts on top of the machine. Faulty equipment must not be used. |
| OPERATIONAL SAFETY PRECAUTIONS Never leave the machine running unattended. Before making adjustments switch off and bring the machine to a complete standstill. Feeding must be against the direction of rotation. Deep cuts should not be attempted. Feed work slowly into the cutter. Jigs, fixtures and templates should be used wherever possible. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.