| Thicknesser | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 079SOP | 080RA |
| DO NOT use / operate / this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Rotating & moving parts - timber may be flung back violently / Pinch & squash injuries / Flying chips and debris / Eye injuries / Excessive noise |
| PRE-OPERATIONAL SAFETY Check workspaces and walkways to ensure that no slip/trip hazards are present. Check material to be planed for defects, splits, dead knots, or contaminants. Ensure in-feed table is clear of debris and free from gum or resin residue. Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop. Do not exceed maximum 2mm depth of cut. Ensure all locks are securely tightened before operating the machine. Start the dust extraction unit before using the machine. Faulty equipment must not be used. Immediately report suspect machinery. |
| OPERATIONAL SAFETY PRECAUTIONS Never leave the machine running unattended. Timber less than 300 mm in length must not be planed on this machine. Feed timber to machine with the grain. Feed only one piece of timber at a time. Never look through machine feed opening when cutter block is revolving. Never plane any timber with embedded nails, and other contaminants. Stand to one side of material being fed through machine in case of kickback. Before making adjustments or before clearing the in-feed or out-feed tables switch off and bring the machine to a complete standstill. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.