| 3D Printer | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 020SOP | 021RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Electricity, Extreme Temperatures, Mechanical, Fire, Hazardous Chemicals |
| PRE-OPERATIONAL SAFETY Check for obvious faults and defects. Check the item has a current electrical test tag attached. Faulty equipment must not be used. Immediately report it. Ensure the risk assessment has been completed. Ensure no slip / trip hazards are present in the workspace and walkways. Locate and ensure you are familiar with the operation of the ON/OFF switch. Ensure print board is securely clipped onto the platform. Ensure the room is well ventilated with circulating air. Printer is located on a level, stable surface. |
| OPERATIONAL SAFETY PRECAUTIONS Switch on computer and login using the credentials located on the computer. Switch on the printer at the rear. Open UP! 3D printer software located on the desktop. Press the initialise button on the printers touch screen. Ensure the printer and filament spool is positioned correctly. Preheat the platform using the printer software. Ensure you have sufficient material on the spool and the allocated time available for the print job. Close doors and covers on the printer prior to starting print job. Keep fingers and foreign objects clear of the moving printer head. Before handling, allow sufficient time for the parts to cool once printing is complete. Do not touch the nozzle, print board or printed model by hand. Wear heat resistant gloves and safety glasses when handling the printer and model. Do not remove the model from the print board while the print board is still attached to the printer. Do not open printer doors whilst printing. When changing a filament spool, follow the manufacturer’s extraction and retraction guidelines. |
| HOUSEKEEPING Gently guide the printing platform out once printing has finished and printer is switched off. Save your work and shutdown the computer. Return all tooling and safety equipment to correct storage location. Leave the machine and work area in a safe, clean and tidy state. Dispose of waste material appropriately. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.