| Laser Cutter | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 021SOP | 057RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Fire, Electricity, Hazardous Chemicals, Radiation, Extreme Temperatures and Mechanical |
|  | Put in Picture of equipment / plant |
| PRE-OPERATIONAL SAFETY Check all software and machine settings carefully before commencing any cutting operation. Check operating lenses are clean. Check nozzle has no build-up of material on it. Load and position the material on the table. Ensure the access door is closed before starting the laser cutter. Ensure air assist has commenced automatically when machine is switched on. Some materials may produce toxic fumes. Check Safety Data Sheet (SDS) prior to use. Ensure power cords are positioned to avoid creating a trip hazard. Faulty equipment must not be used. Immediately report suspect machinery to Tech Studies Coordinator. |
| OPERATIONAL SAFETY PRECAUTIONS DO NOT place any reflective metals into the laser cabinet as the beam may be reflected out and cause injury. DO NOT LEAVE THE MACHINE UNATTENDED WHEN IN USE A CO2 fire extinguisher is available adjacent the machine. Check that fumes / smoke is being extracted through the filter system when machine is operating. Only permissible material is to be cut. If unsure if a material is suitable for laser cutting – DO NOT PROCEED, refer to operating manual. DO NOT operate the machine if any safety features have been modified, disabled or removed. DO NOT open the lid until the fan and light have ceased operating. DO NOT store tools or parts on the machine. |
| HOUSEKEEPING Remove all off cuts and waste, sweep/vacuum the area. Leave the machine and work area in a safe, clean & tidy state. Return surplus material to stock and dispose of waste material in the appropriate recycling or waste bins. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.