| Whipper Snipper - Petrol | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 025SOP | 054RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Fire, Mechanical, Hazardous Chemicals, Hazardous Manual Tasks, Gravity, Noise, Extreme Temperatures |
| PRE-OPERATIONAL SAFETY Check unit for loose/missing nuts/parts. Inspect fuel lines and tank for leaks. Ensure that all guards are fitted and secure. Ensure the harness is attached. Ensure cutting tool is fitted correctly. If using the nylon line cutting head ensure line is correct dimensions. Faulty equipment must not be used. Tag out and report suspect machinery immediately. Keep any person or animal a minimum 15 metre radius away from the working area. |
| OPERATIONAL SAFETY PRECAUTIONS Adjust the handle/s to a position for comfort and good balance. When starting, ensure the line or blade cannot contact the ground or any other obstruction. The muffler side of the engine should be away from your body to avoid burns. Maintain footing and balance at all times. DO NOT work on slippery, uneven or unstable surfaces. Maintain a straight wrist position Avoid using your wrist in a bent, extended or twisted position for extended periods. Always keep both hands on the control handles. DO NOT operate one-handed. DO NOT raise the line or blade head above knee height. Keep machine clear of fences, wires, posts, rocks, etc. to prevent kick out and cutter head damage. Shut down immediately if the unit starts to shake or vibrate. After shutting down the engine, keep fingers and feet away from the cutting line or blade until all rotation stops. Disconnect spark plug wire before you work on the unit or leave it unattended. Take extreme caution when refuelling to avoid igniting fuel on hot exhaust or engine. |
| HOUSEKEEPING Remove any foreign material from engine, cutting tool and guards, once cooled down. Keep the work area and implement shed in a clean and tidy condition. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.