| Hedge Trimmer - Petrol | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 027SOP | 054RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Mechanical, Hazardous Chemicals, Hazardous Manual Tasks, Gravity, Noise, Fire, Extreme Temperatures |
| PRE-OPERATIONAL SAFETY Check for obvious faults and defects. If fuel leaks are identified do not start the machine until the leak is fixed. Identify ON/OFF switch. Cutting blades have a resin solvent sprayed on them for lubrication. Adjust any harness or handles to suit your height and reach. Wear adequate and appropriate PPE. Inspect hedge for any obstacles that may become entangled in the cutting blade. Check fuel level and refuel in well ventilated areas. Wipe up any spilt fuel. If fuel is spilt on clothing, change before use. |
| OPERATIONAL SAFETY PRECAUTIONS DO NOT drop start the machine, place it on the ground to start. Only operate the machine in the open to avoid effects of the exhaust fumes. Transport the machine with the scabbard on and the blade facing away from you. Hold trimmer firmly with both hands and ensure firm footing. If excessive dust is present use an appropriate respirator. Move your body with the trimmer; do not twist from the waist. DO NOT cut over shoulder height. DO NOT walk with trimmer whilst cutter is spinning. DO NOT use in the rain or wet conditions. Ensure bystanders are at least 5 metres away from your working position. If using the machine for prolonged periods take breaks to avoid tiredness and fatigue. DO NOT touch the gearbox housing to avoid burns. |
| HOUSEKEEPING Ensure cutters have stopped before removing waste material Ensure cutters have stopped before placing trimmer on the ground. Clean the cutting blade with a resin type solvent. Ensure equipment is returned to storage area after use and stored safely. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.