| Hedge Trimmer - Electric | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 028SOP | 053RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Mechanical, Hazardous Chemicals, Hazardous Manual Tasks, Gravity, Noise |
| PRE-OPERATIONAL SAFETY Check for obvious faults and defects including electric cord (if not battery powered) for signs of wear or damage. Equipment has current test and tag (if not battery powered). Identify ON/OFF switch/s. Wear appropriate PPE. |
| OPERATIONAL SAFETY PRECAUTIONS Transport the machine with the scabbard on and the blade facing away from you. Hold trimmer firmly with both hands. Ensure firm footing. If excessive dust is present use an appropriate respirator. Move your body with the trimmer; do not twist from the waist. Keep cord free from cutting blades at all times (if fitted) DO NOT cut over shoulder height. DO NOT walk with trimmer whilst blades are moving DO NOT use in the rain or wet conditions. Ensure bystanders are at least 5 metres away from your working position. If using the machine for prolonged periods take breaks to avoid tiredness and fatigue. |
| HOUSEKEEPING Ensure cutters have stopped before removing waste material Ensure cutters have stopped before placing trimmer on the ground. Clean the cutting blade with a resin solvent. Ensure equipment is returned to storage after use and safely stored. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.