| Blower Vacuum - Petrol | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 030SOP | 005RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Mechanical, Hazardous Chemicals, Hazardous Manual Tasks, Gravity, Noise, Fire, Extreme Temperatures |
| PRE-OPERATIONAL SAFETY Jewellery, loose clothing and hair to be secured so that it cannot be drawn into the air inlet. Check machine for loose/missing nuts, bolts and screws. Tighten and/or replace as needed. Inspect the parts of the mulching cutting head (where fitted). Ensure the debris bag (where fitted) is in sound condition and is properly fitted with no gaps. Ensure all guards are fitted, secure and functional. Faulty equipment must not be used. Immediately report suspect machinery. Ensure all other persons are clear of the immediate work area. Fuel the blower when cool and before starting work. |
| OPERATIONAL SAFETY PRECAUTIONS Ensure no person or animal is endangered when operating equipment. Adjust the shoulder harness as required to ensure it is in the most comfortable position. Keep a firm grip. Hold handles with fingers together encircling handles. Maintain a straight wrist position. Avoid using your wrist in a bent, extended or twisted position. Maintain footing and balance at all times. DO NOT stand on slippery, uneven or unstable surfaces. DO NOT work in odd positions or on ladders. Select the mode indicator to adjust the nozzle position for blow or vacuum. DO NOT direct the blower in the direction of other people. Take wind conditions into account. Avoid open doors and windows. Minimise dust by using blower at lower speeds. If the blower vacuum starts to vibrate abnormally, switch off and check immediately. Allow the engine and muffler to completely cool before refuelling or performing any maintenance. Switch off before removing or replacing the debris bag (where fitted). DO NOT place hands in bag when emptying. Sharp debris can cause injury. |
| HOUSEKEEPING Turn off fuel supply when work completed. Remove any foreign material from motor air inlet and nozzle Allow blower to fully cool before putting away. |
| Date of last review: | Signature: |

Acknowledgement much of the information in this document has been sourced by the Department of Education & Children’s Services SA.