| TruSens 2000 / 3000 Air Purifiers (Auto Operation with remote sensor) | SOP Number: | RA Number: |
| --- | --- | --- |
|  | 95SOP | 113RA |
| DO NOT use / operate this equipment or complete the task unless you have been trained. |
| POTENTIAL RISKS: Skin Damage; Eye Damage, Electric Shock, Strains, Sprains, Lacerations, Pinch Points. |
| PRE-OPERATIONAL SAFETY Remove all packaging, including the filter bag, before use. Appliances that are obviously damaged must not be operated. This appliance must only be connected to a wall socket outlet matching the supply plug type and rating stated on the rating plate. Before switching on, check that the unit, remote sensor and power cords are not damaged. |
| OPERATIONAL SAFETY PRECAUTIONS Locate air purifier near the outlet wall socket and do not use extension cords. Plug the remote sensor (SensorPodTM) into a power outlet on the opposite side of the room, ensuring the air purifier is 3 – 15 metres apart and that are in the line-of-sight. Only use the purifier and SensorPod™ with the power cable provided. Switch the air purifier unit on by pressing the on/off button; the unit will take several seconds to boot up. The centre console will indicate the air quality – blue 0-50 = good; yellow 50 – 100 = moderate; red 100 – 500 = poor. Fan speed will automatically adjust. Ensure the UV on/off indicator is lit, this indicates that the UV air sterilisation function is operating. Only clean this machine with a damp cloth, do not use solvents or bleach. Ensure appliance is always placed on firm level surface before operation. Do not block or obstruct the air intake or outlet vents. Do not insert fingers or other items into the air intake or outlet vents. When the air purifier is in standby mode the SensorPod is still transmitting a signal/data. At the end of the school day, switch the unit off, switch off the power outlets. |
| HOUSEKEEPING Switch off the machine. Leave the machine in a safe, clean and tidy state. Do not attempt to service or repair this product yourself |
| Date of last review: | Signature: |

Acknowledgement: much of the information in this document has been sourced by the Department of Education & Children’s Services SA.